## Slide 1
Overview of Computer Networks
Reasons for Studying Computer Networks
Key Components of Computer Networks
Challenges in the Field of Networking
Networking and Communication Application
Benefits of Computer Networks
Responsibilities of a Network Engineer
INTRODUCTION TO COMPUTER NETWORKS

## Slide 2
When two or more computers are linked together with a medium, data can be transmitted and resources can be shared. The computers can be geographically located anywhere. A transmission system is necessary to move bits between systems. A network is a set of devices connected by communication links to communicate and share resources (information).
A computer network is a system that connects multiple computing devices (such as computers, servers, routers, switches, and other hardware) to share data, resources, and services. It allows communication and resource-sharing between different devices, enabling the exchange of information in various forms like text, images, audio, and video.
OR
The term computer network can be defined as two or more computers that are connected to share resources such as data, software, files, internet connection, printers, scanners, etc. The interconnection of various computer systems can be located at different places.
OVERVIEW COMPUTER NETWORK
Figure 1: A typical Network

## Slide 3
OVERVIEW COMPUTER NETWORK
Computer networks are fundamental to modern communication, enabling businesses, governments, and individuals to share resources, collaborate, and access services on a global scale. Whether through local area networks or the vast infrastructure of the Internet, networking is critical for everything from day-to-day business operations to personal entertainment and social interaction.
To build and connect computer networks, clients, and servers, special network infrastructure devices like switches, routers, firewalls, etc. are used.
Network devices follow special protocols to send and receive data over the network. It is capable of delivering voice, video, and data services over the same communication channel or network structure.
Studying computer networks is essential for a wide range of reasons, as networking technology is fundamental to how modern society communicates, shares information, and operates.

## Slide 4
Bandwidth: The maximum data transfer rate of a network, measured in bits per second (bps).
Latency: The time it takes for a data packet to travel from the source to the destination, measured in milliseconds.
Throughput: The actual amount of data transmitted successfully over the network.
Packet Loss: The percentage of data packets that fail to reach their destination, which can degrade network performance.
NETWORK PERFORMANCE METRICS

## Slide 5
Studying computer networks equips individuals with essential skills that are relevant in a wide variety of careers, industries, and technological advancements. Whether it's improving communication, ensuring cybersecurity, or supporting emerging technologies, networking expertise is critical in the modern digital age.
Foundation of Modern Communication (Global Connectivity, Collaboration and Information Sharing)
Career Opportunities (Growing Demand in IT and Networking Jobs)
Understanding Internet and Web Functionality (How the Internet Works, Web Services and Cloud Technology)
Cybersecurity Awareness (Security of Data and Communication, Combat Cyber Threats)
Development of Problem-Solving and Analytical Skills (Troubleshooting Network Issues, Logical and Structured Thinking)
Support for Emerging Technologies (Internet of Things (IoT), Artificial Intelligence (AI) and Machine Learning, 5G and Telecommunications)
Efficient Resource Management (Sharing Resources Efficiently, Data Center and Cloud Infrastructure Management)
Prepare for Future Trends (Smart Cities and Automation, Blockchain and Decentralized Systems, and Quantum Networking)
REASONS FOR STUDYING COMPUTER NETWORKS

## Slide 6
CLASSIFICATION OF COMPUTER NETWORKS
Networks are classified based on various factors like Geographical span, Inter-connectivity, Administration, Architecture, etc.
Geographical Span: Geographically a network can be seen in one of the following categories:
It may be spanned across your table, among Bluetooth-enabled devices, Ranging not more than a few meters.
It may be spanned across a whole building, including intermediate devices to connect all floors.
It may be spanned across a whole city.
It may be spanned across multiple cities or provinces.
It may be one network covering the whole world.
Inter-Connectivity: Components of a network can be connected to each other differently in some fashion. By connectedness, we mean either logically, physically, or both ways.
Every single device can be connected to every other device on the network, making the network mesh.
All devices can be connected to a single medium but geographically disconnected, creating a bus-like structure.

## Slide 7
Each device is connected to its left and right peers only, creating a linear structure.
All devices are connected together with a single device, creating a star-like structure.
All devices connected arbitrarily using all previous ways to connect each other, resulting in a hybrid structure.
Administration: From an administrator’s point of view, a network can be a private network that belongs to a single autonomous system and cannot be accessed outside its physical or logical domain. A network can be public and accessed by all.
Architecture: Computer networks can be discriminated into various types such as client-server, peer-to-peer, or hybrid, depending upon their architecture.
There can be one or more systems acting as servers. The other is the client, which requests the server to serve requests. The server takes and processes requests on behalf of clients.
Two systems can be connected point-to-point, or in a back-to-back fashion. They both reside at the same level and are called peers.
There can be a hybrid network that involves network architecture of both the above types.
CLASSIFICATION OF COMPUTER NETWORKS

## Slide 8
A network must be able to meet a certain number of criteria. The most important of these are performance, reliability, and security.
Performance: Performance can be measured in many ways, including transit time and response time. Transit time is the amount of time required for a message to travel from one device to another. Response time is the elapsed time between an inquiry and a response. The performance of a network depends on several factors, including the number of users, the type of transmission medium, the capabilities of the connected hardware, and the efficiency of the software. Performance is often evaluated by two networking metrics: throughput and delay. We often need more throughput and less delay. However, these two criteria are often contradictory. If we try to send more data to the network, we may increase throughput but we increase the delay because of traffic congestion in the network.
Reliability: In addition to the accuracy of delivery, network reliability is measured by the frequency of failure, the time it takes a link to recover from a failure, and the network's robustness in a devastation.
NETWORK CRITERIA

## Slide 9
Security: Network security issues include protecting data from unauthorized access, protecting data from damage and development, and implementing policies and procedures for recovery from breaches and data losses.
NETWORK CRITERIA

## Slide 10
KEY COMPONENTS OF COMPUTER NETWORKS
Computer networks consist of several key components that work together to enable communication, data sharing, and resource management across connected devices. Each component plays a specific role in the network infrastructure. Understanding these components helps in designing, managing, and troubleshooting networks, which are essential for supporting modern communication and business operations.
Nodes (End Devices): These are the devices that directly connect to a network and communicate with each other. Nodes can be anything from computers and smartphones to printers and sensors. Examples include: workstations/PCs, Servers, mobile Devices, etc.
Network Interface Card (NIC): A hardware component that allows a device to connect to a network. Every device in a network must have a NIC to send and receive data. Examples include: ethernet NIC (wired networks), wireless NIC (Wi-Fi)
Transmission Media (Wired and Wireless): A medium through which data is transmitted in a network. It can be either wired or wireless. Examples include: twisted pair cable, coaxial cable, fiber optic cable, radio wave, microwaves, satellite

## Slide 11
Modem (Modulator-Demodulator): A device that converts digital data from a computer into a format suitable for transmission over analog mediums, like phone lines or cable systems, and vice versa. It enables devices to access the Internet by converting digital signals to analog signals and analog signals to digital signals. This is often integrated into home routers provided by ISPs.
Access Points (AP): A wireless networking device that allows wireless devices to connect to a wired network using Wi-Fi. In Wi-Fi networks, access points serve as a bridge between wireless devices and the wired network. They are essential for setting up wireless LANs.
Firewalls: A network security device that monitors and controls incoming and outgoing network traffic based on security rules. Firewalls help protect networks from unauthorized access, malware, and other security threats by filtering traffic between trusted and untrusted networks. Types of firewalls include hardware firewalls (Standalone devices often used in larger networks) and software firewalls (Installed on individual devices to protect them from threats)
KEY COMPONENTS OF COMPUTER NETWORKS

## Slide 12
Bridges: A device that connects two or more network segments, making them function as a single network. Bridges filter traffic between different network segments and can reduce collisions by dividing a network into smaller collision domains.
Gateways: A network node that acts as a passage between two networks using different communication protocols. Gateways allow devices on various networks to communicate with each other by translating data between the different protocols or systems. A gateway between a home network and the Internet
Repeaters: A device that amplifies or regenerates signals in a network to extend its range. Repeaters are used to prevent signal degradation in long-distance communication by boosting the signal strength.
Network Protocols: Set rules or standards that define how data is transmitted and received across a network. Protocols ensure that devices can communicate effectively. Common Protocols include TCP/IP (Transmission Control Protocol/Internet Protocol): The foundational suite for Internet communication, responsible for routing and addressing packets of data. HTTP/HTTPS (Hypertext Transfer Protocol) is used for accessing websites (HTTPS is the secure version), FTP (File Transfer Protocol) is used for transferring files across a network, SMTP (Simple Mail Transfer Protocol) is for sending emails, DNS (Domain Name System): Translates domain names into IP addresses for network routing.
KEY COMPONENTS OF COMPUTER NETWORKS

## Slide 13
KEY COMPONENTS OF COMPUTER NETWORKS
Switches: A networking device that connects devices within a LAN (Local Area Network) and uses MAC addresses to forward data to the correct device. Switches filter and forward data to the intended recipient device rather than broadcasting it to all devices on the network, making the network more efficient.
Hubs: A basic networking device that connects multiple Ethernet devices, making them act as a single network segment. Unlike switches, hubs broadcast data to all connected devices, making them less efficient. They are rarely used today in modern networks, replaced by more efficient switches.
Routers: A device that routes data between different networks. Routers connect multiple networks together, such as a home network and the Internet. Routers forward data packets between networks based on IP addresses. They also manage traffic and ensure data is transmitted efficiently.

## Slide 14
The client is the term used to describe a workstation, a normal desktop computer, or a laptop, which an end user uses to perform his/her normal duties in the office. The term client computer is used to refer to any device which participates in the network. A server provides resources to other computers on the network. Clients are simple and numerous and they request service from the server. Examples of a client software include internet explorer, firefox, opera, etc.
The client computer establishes a connection to a Server computer and accesses the services installed on the Server Computer.
A Server computer is installed with the appropriate operating system and related software to serve the network clients with one or more services continuously without a break.
CLIENT AND SERVER COMPUTER
Figure 2: A Laptop

## Slide 15
A typical computer network uses different types of servers. Examples of servers used in a network are:
File server
Print server
Database server
Mail server
Domain Name System (DNS) server
Dynamic Host Configuration System (DHCP) server
Video streaming services, etc.
An unexpected shutdown of a server may cause the entire operation of a business down. Above is a rack-mountable Dell server. Each server requires separate server software.
CLIENT AND SERVER COMPUTER
Figure 3: A Server

## Slide 16
As the organization's network grows, it must gradually upgrade its peer-to-peer network to a client-server-based network. A client-server computer network model is made up of client computers and server computers. In a client-server network, high-end servers are installed with the network operating system (server operating system) and the related software to serve the clients continuously on a network by providing them with specific services upon request.
Well-known server operating system products are Microsoft Windows Server 2019, Oracle Solaris, Ubuntu server, Net BSD, Open BSD, etc.
File Server: File servers are used to store the user documents and files centrally. An ideal file server should have a large amount of memory and storage space, fast hard disks, multiple processors, fast network adapters, redundant power supplies, etc. A File server runs File Transfer Protocol (FTP) in Windows, Linux, or Unix Networks, or Server Message Block Protocol (SMBP) in Windows Networks. Well-known FTP software products are Microsoft Internet Information Services (IIS), FileZilla Server, Apache FTP Server, etc.
CLIENT SERVER NETWORKS

## Slide 17
CLIENT SERVER NETWORKS
Print Server: Print Server redirects print jobs from client computers to specific printers
Mail Server: Mail Servers are used to transmit emails using email protocols. The most widely used email transmission protocol is the Simple Mail Transfer Protocol (SMTP). Mail Servers exchange emails between different domains. The Most widely used Mail Server software products are Microsoft Exchange Server, SENDMAIL, Postfix, Apache James, etc.
Application Server: Common computer applications or programs that are required by different network users can be run on a central server, which enables multiple network users to access common network applications from the network. Some examples of Application Server Software are SAP ERP, Microsoft Dynamics, Oracle ERP Cloud, Ramco ERP, Infor ERP, etc.

## Slide 18
CLIENT SERVER NETWORKS
Database Server: Database Servers allow authorized network clients to create, view, modify, and/or delete an organization's data, stored in a common database. Examples of Database Management Systems include Oracle Database Products, Microsoft SQL Server 2019, PostgreSQL, IBM DB2 Database Server, MySQL Database Server, Informix, MongoDB, MariaDB Server, etc.
Directory Servers: Directory Servers allow the central administration and management of network users and network resources. Directory Servers provide the basic functions of network security, Authentication, Authorization, and Accounting. Examples of Directory Servers are Microsoft Active Directory, NetIQ eDirectory, Fedora Directory Server, OpenLDAP, etc.

## Slide 19
The four main principles of a network include the following:
Each computer must have a network interface to provide a doorway for information
The network usually has at least one connecting device
The network must have communication media to transport information
Each computer must have software to move information in and out of the computer
These four principles apply to all networks, large and small.
BASIC PRINCIPLES OF NETWORKS
KEY COMPONENTS OF NETWORKS
Many components can be part of a network. These components can be grouped into four main categories:
Hosts - devices that send and receive messages directly across the network. e.g. PC
Shared peripherals - not directly connected to the network, but instead are connected to hosts. e.g. printers
Networking devices - are used to interconnect hosts. e.g. Hub, Switch, etc.
Networking media - can be wired such as copper and fiber optic or wireless technologies

## Slide 20
INTERNET, INTRANET AND EXTRANET
Internet: The Internet is a worldwide, publicly accessible computer network of interconnected computer networks that transmit data using the standard Internet Protocol (IP). The largest Internetwork in the world is the Internet.
Intranet: An intranet is a private network that is contained within an enterprise. A typical intranet for an organization consists of many interlinked local area networks (LAN) and uses any Wide Area Network (WAN) technology for network connectivity. The main purpose of an intranet is to share company information and computing resources among employees. The content available inside the Intranet is intended only for the members of that organization (usually employees of a company).
Extranet: An extranet can be viewed as part of a company's intranet that is extended to users outside the company like suppliers, vendors, partners, customers, or other business associates. An extranet is required for normal day-to-day business activities. For example, placing a purchase order to registered vendors, billing and invoices, payments-related activities, joint venture-related activities, product brochures for partners, discounted price lists for partners, etc.

## Slide 21
METHODS OF INTERNET CONNECTIONS
Many homes and small business users connect to the Internet via high-speed broadband Internet service:
Cable Internet service: provides high-speed Internet access through the cable television network via a cable modem.
Digital Subscriber Line (DSL): provides high-speed Internet connections using regular copper telephone lines.
Fiber to the Premises (FTTP): uses fiber-optic cable to provide high-speed Internet access to home and business users.
Fixed wireless: provides high-speed Internet connections using a dish-shaped antenna on your house or business to communicate with a tower location via radio signals.
Cellular Radio Network: offers high-speed Internet connections to devices with built-in compatible technology or computers with wireless modems.
Wi-Fi network uses radio signals to provide high-speed Internet connections to compatible or properly equipped wireless computers and devices.
Satellite Internet Service: provides high-speed Internet connections via satellite to a satellite dish that communicates with a satellite modem.

## Slide 22
Client and server software usually runs on separate computers, but it is also possible for one computer to carry out both roles at the same time. In small businesses and homes, many computers function as servers and clients on the network. This type of network is called a peer-to-peer network. A peer-to-peer network has no dedicated servers. In a peer-to-peer network, several workstations (or clients) are connected to share devices, information, or data.
The Microsoft term for the peer-to-peer network is called “Workgroup”. All the workstations (clients) are considered equal. Any computer can act as a client or server at any instance. This network is ideal for small networks where there is no need for dedicated servers, like home networks, small business networks, retail shops, small pharmacy outlets, automobile service centers, small clinics, etc.
The simplest peer-to-peer network consists of two directly connected computers using a wired or wireless connection. Multiple PCs can also be connected to create a larger peer-to-peer network but this requires a network device, such as a hub, to interconnect the computers.
PEER-TO-PEER NETWORKS

## Slide 23
ADVANTAGES AND DISADVANTAGES OF PEER-TO-PEER NETWORKS
Advantages | Disadvantages
1. Easy to setup | 1. No centralized administration (Everything is kept distributed in different computers)
2. Less complexity | 2. Managing network users is extremely difficult.
3. Low cost | 3. User generated files are stored in individual computers
4. Can be used for simple tasks e.g. transferring files and sharing printers | 4. All devices may act as both clients and servers which may slow their performance

## Slide 24
Most network communication starts with a user needing to access a resource on another computer, such as a Web server or file server. A user’s attempt to access network resources is summarized in these basic steps:
An application tries to access a network resource by attempting to send a message to it.
Network client software detects the attempt to access the network. Client software formats the message generated by the application and passes the message on to the network protocol.
The protocol packages the message in a format suitable for the network and sends it to the NIC driver.
The NIC driver sends the data in the request to the NIC card, which converts it into the necessary signals to be transmitted across the network medium.
STEPS OF NETWORK COMMUNICATION

## Slide 25
Remember that there are two sides to a communication session, and most of them involve a client trying to access network resources and a server providing those resources. The steps taken on the server side are essentially the reverse of those on the client side:
The NIC card on the server receives signals from the network medium and converts them into message data, which is read by the NIC driver.
The NIC driver passes the message to the network protocol.
The network protocol determines which server software the message is targeting and passes the message to this designated software.
The server software receives the message and responds by sending the requested data to the client’s computer, using the four steps outlined previously.
STEPS OF NETWORK COMMUNICATION

## Slide 26
CHALLENGES IN THE FIELD OF NETWORKING
    The field of networking faces several challenges, driven by rapid technological advancements, increasing demand for connectivity, and the growing complexity of modern networks. These challenges affect the design, management, security, scalability of networks, etc.
    Network Congestion/ Performance degradation: Network congestion occurs when too many devices or data requests overload network resources, leading to slow performance, packet loss, or timeouts. Congestion can severely degrade the user experience, causing issues like dropped connections during video calls, slow website loading, and buffering in media streams. Managing traffic efficiently and implementing effective congestion control mechanisms is critical.
    Security: Security issues increase with the increase in network size. Maintaining network security requires constant vigilance and the ability to respond to evolving threats. Blocking unauthorized outside traffic is not enough to protect data. Many threats make it into the network when employees respond to phishing emails and insider attacks. Even with advanced firewalls, intrusion detection systems (IDS), and encryption, attackers continue to find new ways to breach networks.

## Slide 27
Network Automation and Management: Manually configuring and managing large, complex networks is time-consuming and error-prone. There is a growing need for automated network management tools that can handle tasks such as configuration, monitoring, and troubleshooting.
Network Interoperability: Networks often involve equipment and software from different vendors, using different technologies and protocols. Ensuring that these components can work together seamlessly is a significant challenge. Lack of interoperability can lead to compatibility issues, higher costs for integration, and operational inefficiencies. Vendors typically use proprietary solutions that make it hard for different systems to communicate without specialized adapters or configurations.
IPv4 to IPv6 Transition: The IPv4 which has been the dominant addressing system for decades is being replaced with IPv6. The coexistence of both IPv4 and IPv6 networks creates challenges in terms of compatibility, management, and configuration. Full migration to IPv6 is essential to accommodate future growth in connected devices but requires significant infrastructure updates.
CHALLENGES IN THE FIELD OF NETWORKING

## Slide 28
Complex Network Management: As networks grow larger and more complex, managing them becomes increasingly difficult. This includes handling diverse device types, heterogeneous network environments, and hybrid infrastructures that combine cloud, on-premises, and edge components. Network administrators face the challenge of configuring, monitoring, and troubleshooting large-scale, multi-vendor networks. Traditional manual network management approaches become inadequate, leading to the need for automation tools and Software-Defined Networking (SDN) solutions.
Bandwidth and Latency Constraints: Many modern applications, such as video streaming, cloud computing, virtual reality (VR), and online gaming, require high bandwidth and low latency. Networks must meet these demands while avoiding congestion and packet loss. Ensuring consistent performance across distributed networks, especially when dealing with high-data-rate applications, is difficult. Network providers must constantly upgrade infrastructure to support high-speed connections and minimize latency.
CHALLENGES IN THE FIELD OF NETWORKING

## Slide 29
CHALLENGES IN THE FIELD OF NETWORKING
    Cost: As more business functions move onto the network, companies need to upgrade their network and add capacity and new capabilities. Networks have to handle other business services like telephony, video conferencing, and multimedia applications, which require improved network bandwidth which is expensive.
    Scalability: As the number of devices connected to networks increases exponentially (due to IoT, smartphones, cloud computing, etc.), ensuring that networks can scale to handle this growth is a major challenge. Larger networks require more complex management, increased bandwidth, and higher efficiency. Traditional networking infrastructure may struggle to meet these needs, leading to performance bottlenecks, congestion, and network failures.

## Slide 30
Computer networking and communication applications are essential to modern business operations, entertainment, social interaction, and personal productivity. They enable seamless communication, collaboration, content sharing, and access to services over local, wide-area, and global networks. Networking and communication applications include the following:
  Mobile phones (wireless phones)
  Cellular phones
  Satellite phone
  Wi-Fi phones
  Mobile Video conferencing
  Communications technology for real-time, face-to-face meetings between individuals located in different places
  Online conferencing (via the Internet)
  Video conferencing/video phone calls
NETWORKING AND COMMUNICATIONS APPLICATIONS

## Slide 31
NETWORKING AND COMMUNICATION APPLICATIONS
  Collaborative computing (workgroup computing): using a computer and communications technology to work together on documents and other project components
  Global positioning system (GPS): Uses satellites and a receiver to determine the exact geographic location of the receiver
  Commonly found in cars today and available as handheld units
  Used by the military, hikers, travelers, and others who need to know their precise location
  Telecommuting: individuals work at home and communicate with their place of business and clients via communications technologies.
  Digital data distribution: transferring digital data (digital photos, music, movies, TV broadcasts, medical imaging files, etc.) electronically from one place to another
  Home use, Business use, Digital movie distribution, etc.

## Slide 32
NETWORKING AND COMMUNICATIONS APPLICATIONS
Monitoring systems - monitor the status of or location of individuals, vehicles, assets, etc.
Electronic medical monitors
GPS-based monitoring systems
RFID short-range monitoring systems
Monitoring via the Internet-Satellite radio - delivers digital radio content to satellite receivers, which can be car-mounted, placed in the home, carried around
Internet of Things (IoT) Applications - (smart home systems, industrial IoT)
Email and Messaging Services- (email, instant messaging, and chat applications)

## Slide 33
Computer networks allow the user to access remote programs and remote databases either of the same organization or from other enterprises or public sources.
Computer networks allow users to communicate using e-mail, newsgroups, video conferencing, etc.
Resource Sharing (hardware sharing, applications, file and data sharing)
Greater flexibility because of the possibility to connect devices from various vendors.
Doing business electronically (B2B, B2C). Advertise and sell products, order supplies, and communicate with customers.
Network games are available that allow multi-users to play from different locations.
Desktop sharing lets remote workers see and interact with a graphical computer screen. This makes it easy for two or more people who work far apart to read and write a shared blackboard or write a report together. When one worker makes a change to an online document, the others can see the change immediately, instead of waiting several days for a letter.
BENEFITS OF COMPUTER NETWORKS

## Slide 34
Voice over Internet Protocol (IP) is a revolutionary change in telecommunication that allows users to send telephone calls (voice data) using standard Internet Protocol (IP).
Improves health care delivery
Enhance research and online learning
Data Security and Centralized Management (centralized data security, user authentication, and access control)
Improves Communication (real-time communication, email, and social media)
Access to Cloud Services (cloud computing, data storage)
BENEFITS OF COMPUTER NETWORKS

## Slide 35
  Determines how much bandwidth is required for the smooth operation of the organization’s network
  Enabling Communication Between Devices (data transfer and communication protocols, interconnectivity of systems)
  Facilitating Network Security (Securing Data Transmission, Cybersecurity Solutions)
  Developing and Managing Network Protocols (designing efficient protocols, network performance optimization)
  Enhancing Multimedia and Real-Time Applications (real-time data transmission, multimedia networking)
  Supporting 5G and Telecommunications Advancements (telecommunications networks)
  Configures DHCP server for dynamic IP addressing
RESPONSIBILITIES OF A NETWORK ENGINEER.

## Slide 36
The role of networks in computer engineering spans from enabling communication between devices to supporting the architecture of distributed systems, cloud computing, and modern innovations like IoT (Internet of Things). Responsibilities of a network engineer include:
  Network Upgrades and Optimization (upgrading network infrastructure, implementing New, Technologies, capacity expansion)
  Managing and maintaining the network, internet connectivity, and inter-branch connectivity
  Providing technical support to end users
Designing and setting up an organization’s computer network.
RESPONSIBILITIES OF A NETWORK ENGINEER.

## Slide 37
Define computer networks.
State four responsibilities of a network engineer.
State four benefits of computer networks.
What are the three criteria necessary for an effective and efficient network?
State and explain two challenges in the field of computer networking.
State four (4) characteristics of the Ethernet.
State five (5) servers used by a typical computer network.
Why do we keep network user files and electronic documents in a file server?
READING ASSIGNMENT